AbstractMessage – length: 4 bytes
Field	Offset	Size (byte)	Note, example
Signature	0	1	0x15 = ls = LiveShift
PROTOCOL_VERSION	1	1	1
messageId;	2	1	Wraps over, starts at 1
ReplyMessageId present?	3	1	0=null, 1=not null
replyMessageId	4	1	MessageId this message is a reply for
MESSAGE_TYPE	5	1	B BlockRequestMessage / C BlockReplyMessage / D DisconnectMessage / G GrantedMessage / H HaveMessage / I InterestedMessage / P PingMessage / Q QueuedMessage / S PeerSuggetion / U SubscribeMessage / V SubscribedMessage / X SducSubscribeMessage / J PshDownloadersRequestMessage / K PshDownloadersReplyMessage / L PshCheckRequestMessage / M PshCheckReplyMessage / N PshApplyRequestMessage / O PshApplyReplyMessage

SubscribeMessage – length: 6 + 12 + name.length bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
PeerName	19	1 for size, then 1 per character	Name

SducSubscribeMessage – length: SubscribeMessage+4 bytes
Field	Offset	Size (byte)	Note, example
peerUploadCapacity	SubscribeMessage.size()	4	float

PingMessage – length: 6 + 1 bytes
Field	Offset	Size (byte)	Note, example
Request/reply	6	1	1=request 0=reply

HaveMessage – length: 6 + 22 bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
blockNumber	19	4	int
doHave	23	1	1=have, 0=don't have
rate	24	4	int

DisconnectMessage – length: 6 + 14 bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
stopUploading	19	1 bit	Byte (lsb) / 2. lsb
stopDownloading	19	1 bit

BlockRequestMessage – length: 6 + 17 bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
blockNumber	19	4	int

BlockReplyMessage – length: 31795 bytes (with CBR 500kbit/s in packets of 1500 bytes)
Field	Offset	Size (byte)	Note, example
blockReplyCode	6	1	1 GRANTED, / 2 DONT_HAVE, / 3 REJECTED
SegmentBlock	7 / 20 / 24 / 25 / ( / +8 / +8 / +1 / +4 / +videoData / )	13 / 4 / 1 / 4 / (21+packet length)*packets / packet length max = 1600 / (depends on VLC)	SegmentIdentifier / int blockNumber / hopcount / int number of packets, each with / long timeMS; / long sequenceNo; / byte substream; / int videoData length / byte[] videoData

SubscribedMessage – length: 6 + 18+block map size+name size bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
not	19	1	1 = not subscribed / 0 = subscribed
timeoutMillis	20	4	int
segmentBlockMap	24	[only present if not=0] / X=ceil(BlocksPerSegment/8) / 15 in my tests	SegmentBlockMap
PeerName	24+X	1 for size, then 1 per character	Name

QueuedMessage – length: 6 + 18 bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
not	19	1	1 = not subscribed / 0 = subscribed
timeoutMillis	20	4	int

GrantedMessage – length: 6 + 22 bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
not	19	1	1 = not subscribed / 0 = subscribed
timeoutMillis	20	4	int
timeoutInactiveMillis	24	4	int

InterestedMessage – length: 6 + 14 bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
not	19	1	1=not interested / 0=interested

PeerSuggetion – length 6 + 37+socket size (minimum 11)+peer name size bytes
Field	Offset	Size (byte)	Note, example
SegmentIdentifier	6	13	int channelID / byte substream / long SegmentNumber
numSuggestedPeers	17	1
SuggestedPeer n / DhtAddress	18+x	20 bytes (160 bit)
SuggestedPeer n / SocketAddress	38+x	1 for size (9 if Ipv4, 21 if Ipv6) / 9 if Ipv4, 21 if Ipv6 / 1 for size, then 1 per character	SocketAddress / Name

PSH

PshDownloadersRequestMessage – length: 6 + 20+n*20
Field	Offset	Size (byte)	Note, example
ListSize	x	4	In future maybe use Bloom Filter
PeerIds	x+n*20	20 per peerId

PshDownloadersReplyMessage – length: 6 + 24+n*24
Field	Offset	Size (byte)	Note, example
ListSize		4
PeerIds		20
MaxAmount		4	Maximum willing to trade

PshCheckRequestMessage – length: 6 + 64
Field	Offset	Size (byte)	Note, example
Intermediate dhtId		20
Target dhtId		20
maxAmount		4

PshCheckReplyMessage – length: 6 + 192
Field	Offset	Size (byte)	Note, example
Intermediate dhtId		20
Target dhtId		20
amount		4	float
signatureIntermediate		128	1024 bit

PshApplyRequestMessage – length: 6 + 196
Field	Offset	Size (byte)	Note, example
Intermediate dhtId		20
Target dhtId		20
Amount check		4	float
signatureIntermediate		128	1024 bit
Amount to apply		4	float

PshApplyReplyMessage – length: 6 + 24
Field	Offset	Size (byte)	Note, example
Amount applied	6	4	float